## Slide 1
AROL telemetry report agent
Capping closure data, deterministic analytics and a scoped BOT interface
Software and Device Programming project review

## Slide 2
Project objective
02
Load curated machine telemetry into a consistent event dataset.
Select analytical tools from a user question and generate a report.
Show methods, data scope, limitations and evidence with each result.
Scope: torque and closure diagnostics

## Slide 3
Telemetry and event pool
03
89 CSV files · 7,623,968 raw rows · 36 heads
Each raw row provides timestamp, per-head counter, torque and status.
The builder writes raw and observed-event Parquet partitions plus a manifest.
The manifest records 54,722,936 exact +1 observations across the pool.

## Slide 4
Observed closure construction
04
Per head: compare the counter with its previous observation.
A change of exactly +1 emits one event with the new torque and status.
The previous value carries across files: 667 boundary events were verified.
Jumps and decreases are measured; individual unseen closures are not invented.

## Slide 5
Architecture
05
Offline pool build
CSV readings → validation → counter check → Parquet + manifest
Question and report
CLI query → planner → scoped source → registered tools
Tool results → report + trace + optional figures

## Slide 6
Deterministic analysis tools
06
Torque: statistics, histogram, trailing mean, anomaly flags and head pairing.
KPIs: explicit cap-present success, per-head comparison and time buckets.
Machine-wide No Load: consecutive raw readings on every head.
Reported rates and flags describe observations; they do not prove cause.

## Slide 7
Agent decision flow
07
The rules planner maps supported phrasing to registered tools and filters.
The source reads the selected machine, heads and requested time window.
Tools calculate results; report templates describe the result and its limits.
Ambiguous requests stop for clarification without calling analysis tools.
Optional Ollama routing validates a model proposal against the same scope.

## Slide 8
Sample torque report
08
A synthetic two-file pool
The histogram plots the bin edges and counts returned by the tool.
The same report gives sample size, mean, spread and threshold caveats.

## Slide 9
Success-rate denominators
09
H05, one 12-hour window on the supplied machine
13,167
observed exact +1 events
7,575
confirmed cap-present
5,592
No Load class events
Cap-present success: 7,575 / 7,575 = 100% in this scope.
Status-0 as a fraction of all observed events: 57.53%. Each report labels its denominator.

## Slide 10
All-head No Load intervals
10
Synthetic example:
310 consecutive seconds with No Load on both heads.
Gaps and repeated timestamps break a run. A status pattern alone cannot confirm downtime.

## Slide 11
Verification evidence
11
Uploaded source snapshot: 856 tests passed; 4 standalone-repo tests skipped.
Controlled question set: 28 of 28 cases passed in the prior evaluation.
Planted torque labels: 4 detected, 1 missed, and 0 false positives.
A scoped live Qwen request matched the independent torque calculation.
Controlled results do not estimate reliability on arbitrary questions or physical faults.

## Slide 12
Live demonstration
12
1. Select the completed local pool manifest.
2. Ask for torque statistics and a histogram in a bounded scope.
3. Ask for a per-head KPI or an hourly rate as a second report type.
4. Open the Markdown reports, PNGs and JSON tool-call traces.
Run from a clean checkout; keep original telemetry under ignored data/.

## Slide 13
Interpretation and next checks
13
Counter jumps leave unknown individual closures. Duplicate raw rows remain visible.
No Load and zero observed events need operating context before a downtime claim.
Torque limits and failure definitions require process-owner confirmation.
The agent reports evidence and traceable tool choices; it does not diagnose physical causes.